## Slide 1: Solar Car Suspension
Jarrett Dunn
SOLAR CAR CHALLENGE

## Slide 2: Agenda
Introduction
Suspension Types
Key Terms
Measuring Toe
Ackerman Steering
Best Practices

## Slide 3: Common Front Suspension Types
Solid Axle
MacPherson Strut
Dual A Arm
Notes: MacPherson
-tend to be heavy
-limited adjustability
Solid Axles
-simple
-geometry is set at construction
-can be heavy
Double Arm
-most popular
-very versatile
-can be complicated with lots of options and area for mistakes

## Slide 4: Less Common Suspension Types
Torsion Axle
Radius Arm
Mountain Bike Fork
Solid

## Slide 5: Vocabulary
Contact Patch
  Oval shaped area where tire contacts the road
Steering Axis
  Line between two pivot points of the wheel
Ideal
Top
Side
Real
Top
Side

## Slide 6: Contact Patch
This is where your car interacts with the road
Critical to cars steering, handling, and braking
Effected by tire type, construction, pressure

## Slide 7: Vocabulary
Contact Patch
  Oval shaped area where tire contacts the road
Steering Axis
  Line between two pivot points of the wheel

## Slide 8: Vocabulary
Toe
  Angle of the wheel and tire pointing away from the centerline of the vehicle
Caster
  The angular displacement of the steering angle for the vertical axis
Camber
  The angle of the wheel and tire with respect to the vertical axis
Scrub Radius
  The distance between where the steering angle intersects the ground and the contact patch of the tire

## Slide 9: Toe (Neutral)
Front
Center Line

## Slide 10: Toe (In)
Front
Center Line

## Slide 11: Toe (Out)
Front
Center Line

## Slide 12: Toe
Affects Tire Wear
Toe Out
  Improves Steering Response
  Can make steering “jerky”
Toe In
  Improves straight line stability

## Slide 13: Vocabulary
Toe
  Angle of the wheel and tire pointing away from the centerline of the vehicle
Caster
  The angular displacement of the steering angle for the vertical axis
Camber
  The angle of the wheel and tire with respect to the vertical axis
Scrub Radius
  The distance between where the steering angle intersects the ground and the contact patch of the tire

## Slide 14: Caster (Positive)
Front
Vertical
θ

## Slide 15: Caster
Creates straight line stability
Positive Caster
  Steering wheel feedback
  Makes car harder to turn
  Causes wheels to self center
Negative Caster
  Unstable

## Slide 16: Vocabulary
Toe
  Angle of the wheel and tire pointing away from the centerline of the vehicle
Caster
  The angular displacement of the steering angle for the vertical axis
Camber
  The angle of the wheel and tire with respect to the vertical axis
Scrub Radius
  The distance between where the steering angle intersects the ground and the contact patch of the tire

## Slide 17: Camber (Negative)
Vertical
Front

## Slide 18: Camber (Negative)
Vertical
Front

## Slide 19: Camber
Affects grip and stability in cornering
Not applicable to solar car racing
Camber Gain

## Slide 20: Vocabulary
Toe
  Angle of the wheel and tire pointing away from the centerline of the vehicle
Caster
  The angular displacement of the steering angle for the vertical axis
Camber
  The angle of the wheel and tire with respect to the vertical axis
Scrub Radius
  The distance between where the steering angle intersects the ground and the contact patch of the tire

## Slide 21: Scrub Radius (Positive)
Scrub Radius

## Slide 22: Scrub Radius
Coffee Cup Experiment
Harder to Turn
Increase wear on tire
Positive
  Cause center seeking

## Slide 23: Ackerman Steering

## Slide 24: Measuring Toe
A1
A2
B1
B2
Front
C
Dist A
Dist B

## Slide 25: Measuring Toe
A1
A2
B1
B2
Front
C

## Slide 26: Best Practices
Consistency is key
  Be methodical
  Do the same thing every time
Make Dedicated Tools
Solar car racing is about efficiency
  Small or zero angles
Date | Tire Pressure | Driver | Toe

## Slide 27: References
Tune to Win, Carrol Smith
Design to Win, Carrol Smith
The Winning Solar Car, Douglas R. Carroll
The Leading Edge, Goro Tamai