## Slide 1: Specialty Workshop
Powering the Solar Car

## Slide 2: Powering the solar car
How do you get the car moving?
  Photovoltaic array choices
  Power trackers and DC-DC converters
  Electric motors and controllers

## Slide 3: Arrays

## Slide 4: Substrate and Support Frame
Varies Depending on the Type of Array
Main Considerations
  Rigidity
  Cooling
  Weight
  Conductivity

## Slide 5: Panel Temperature
Solar Cells change efficiency as their temperature changes
https://www.jeroenboeye.com/blog/solar-panel-analysis-pt-2-temperature-and-efficiency/

## Slide 6: Shape of Array
Flat Solar Arrays
  Easier to execute
  Angle to sun less of a concern
  Wing over body vs Canopy Above Array

## Slide 7: Shape of Array
Curved Solar Arrays
  Higher the angle the greater chance for breaks without ideal support.
  Angle to sun more of a concern

## Slide 8: The Solar Array
Pre-made Commercial panels
    Reliable
    More Easily purchased
    Typically HEAVY (glass top adds weight)

## Slide 9: The Solar Array
Premade Lightweight Options
Many more on our website and online…

## Slide 10: The Solar Array
Raw cells and lamination
  Planning has to start FAR in advance (you are probably too late already!)
  Process is expensive
  Panels are very light and can be built to fit your car
  Easy to maximize power and reduce aerodynamic drag
SunCat solar

## Slide 11: Laminated Cells

## Slide 12: The Solar Array
Do-it-yourself solar array
  Amazing learning experience
  Learning curve is steep
  Hard to find raw cells
  Takes a lot of man power
  Hard to watch when cells are continually breaking
  Can fit exactly to your car

## Slide 13: Do-it-yourself

## Slide 14: Do-it-yourself

## Slide 15: Power Trackers (MPPTs)

## Slide 16: MPPTs and DC-DC Converters
Moving power from the solar array to the batteries is not as easy as hooking up a couple of wires!
  Voltage from your solar array needs to match the voltage of the battery pack.
  More often than not the group of solar panels will not match your system / pack voltage
  Even if you do match the pack voltage it will not be efficient for charging your battery pack
  Without protection you can have reverse current flow into the panels when they are shaded

## Slide 17: What MPPTs Do
Maximum Power Point Trackers (MPPTs) adjust voltage and current from your array to give you the most efficient transfer of power to your vehicle
  They adjust the output voltage of your array to always be at the right voltage for ideal charging of your battery
  They can either “boost” voltage (40V to 72V) to a higher value or “buck” voltage (140V to 80V) to a lower value
MPPTs are also a main source of telemetry for your array

## Slide 18: MPPT and DC-DC Choices
AERL (Australian Energy Research Laboratories)
Solar Converters Inc
Outback (and other grid type MPPTs)
Genasun
Nomura Co
Elmar

## Slide 19: AERL MPPTs

## Slide 20: Electric Motors

## Slide 21: Electric Motors
Brushed Electric Motors
  Inexpensive
  Lower overall efficiency
  Controller is inexpensive and easy to wire
Brushless Electric Motors
  Very efficient
  More expensive
  Controller is more difficult to wire (typically 3 phase)

## Slide 22: Brushed Motor Examples
Briggs and Stratton ETEK
Lynch LM200
Perm-Motor PMG-132 12-72 VDC
  90% efficient
  Wide voltage range (12-72 volts)
  Light weight (24 pounds)
  $1400

## Slide 23: Motor Efficiency Data (ME0909)

## Slide 24: Brushed Motor Examples
Motenergy ME0909 Permanent Magnet DC
  Best replacement for original Briggs and Stratton E-tek
  12-48 volt
  Light weight (24 pounds)
  Inexpensive ($450)

## Slide 25: Brushed Motor Examples
Advanced DC K91-4003 motor, 48-96VDC
  Higher voltage motor (48-96 volts)
  Strong motor for heavier cars
  Low cost ($800)

## Slide 26: Brushless Motor Example
Motenergy ME0907 Brushless PMSM/BLDC
  No brushes=no maintenance
  24-72 volts
  Very efficient (over 90%)
  High current (up to 100 amps continuous)
  Motor is inexpensive ($460)
  Special controller needed

## Slide 27: Hub Motor
NGM ‘Direct Drive’ high efficiency in-hub motor with variable air gap adjustment.
  Super efficient over a broad range of speeds
  No need for gears or chain
  Very expensive (Motor + controller > $25,000)
Mitsuba / Nomura hub motors replacing NGM as favored motor for solar car teams
  Still ~$25,000

## Slide 28: Brushed PWM Controller
Alltrax AXE
Easy to wire
0-5k Pot control
Programmable
Durable

## Slide 29: Sevcon controller (Brushless)

## Slide 30: A Brief Interlude on Gearing

## Slide 31: Choose the Correct Gears
Don’t gear a car for 50 mph if you are going to drive it at 25 mph. Be realistic about your cars speed!
Chain drive systems can be very efficient if gears are aligned and lubricated.
Pictured: 48V system, 15 tooth front, 70 tooth rear. Max speed = 36 mph

## Slide 32: Gearing to match your motor
How fast will I go with…
Variable | Defined As
 | Speed in Miles/Hour
 | Target Motor RPM
 | # Teeth Small Sprocket
 | Diameter Wheel in Inches
 | # Teeth Big Sprocket
Variable | Defined As
 | Speed in Miles/Hour
 | Target Motor RPM
 | # Teeth Small Sprocket
 | Diameter Wheel in Inches
 | # Teeth Big Sprocket

## Slide 33: Choose the Correct Gears
Custom Sprockets:
Rocket Sprockets www.rocketsprocket.net
PMP Sprockets www.pmpsprocket.com

## Slide 34: The Electrical System

## Slide 35: Electrical System

## Slide 36: Electrical System
Propulsion System
  Use the correct gauge wire for the job
  Disconnect switches should be designed for DC
  Fuses
Auxiliary electrical system (everything else on your car)
  Lights
  Fans
  Horn

## Slide 37: Electrical Schematics

## Slide 38: Batteries

## Slide 39: Batteries
Choose carefully!
Batteries are one of the areas where you get what you pay for.
  Decisions to make:
    What voltage does your car run at?
      Higher voltage means lower current .
    How much weight can you carry?
    How much energy can you get at that weight?
    Can your solar panels recharge the battery pack?
    Is it a road race or a track race?

## Slide 40: Batteries
The 5 kilowatt-hour rule
  kw-h = Amp-hours x Voltage
  (at the 20 hour discharge rate)
  Example:
  Four, 12 volt, 84 amp-hour batteries in series
  84ah x 48 v = 4032 watt-hours or 4.032 kilowatt-hours
  (this battery pack would weigh around 230 pounds)

## Slide 41: Batteries
Choosing batteries based on the Peukert number:
  A typical sealed lead acid battery has a Peukert number between 1.1 and 1.3. (The closer to 1.0 the better!)

## Slide 42: Batteries
Testing batteries:
  Understanding how your batteries perform is one of the most important things you can know BEFORE the race starts.
  Carefully recording voltage, current, and amp-hours will help your team make good decisions during the race

## Slide 43: Batteries
Some of our favorites:
  Concorde Sun Xtender series
    84 Ah $245/battery
  EnerSys Odyssey Marine series
    68 Ah $250/battery

## Slide 44: Everything Else Electrical

## Slide 45: Switches/Fuses
    There are a lot of resources for switches and fuses. Be sure they meet the race requirements before ordering!
    Be sure they are rated for your DC system. (AC rating will not qualify!)
    (Bussmann FWH Fuses are rated at 500V DC)
    Relays are required!
    Electric Motorsport www.electricmotorsport.com
    Tecknowledgey
    http://www.tecknowledgey.com
Single Pole On/Off Rated load: 400 A Break Current: 1200 A @ 48 V DC (600 A @ 96 V DC)
500V DC @90 amp fuse is about $50

## Slide 46: Low Voltage Indicator
Do-It-Yourself kit available at:
http://store.qkits.com/
Look for “Low Voltage Alarm”
Cots Solution

## Slide 47: Wire
Propulsion System Wire
  Use welding cable
    Should be very flexibly
  Use proper crimping tools and lugs
    Don’t attempt to solder
    Don’t attempt to splice
  Be aware of counterfeit cables
  Be sure to size to your system
Auxiliary System Wire
  Have a variety
  Get higher quality wire with more strands
http://www.flex-innovations.com/counterfeit.htm
Different Strand Configurations
For the same wire gauge

## Slide 48: Heat Shrink
Heat shrink
  Should always be used
  It’s worth it to spring for the 3M heat shrink
  You will need a heat gun
X


## Slide 49: Soldering
Tools Needed
  Wire strippers
    My preference is nothing fancy
  Solder
    Lead free can be used but 60/40 Tin Lead Rosin Core is typical
    There are many diameters
      Very small diameter (0.6mm) solder is not meant for 16 ga / 18 ga wire
      Larger diameter (1.5mm+) solder is not appropriate for fine soldering (like making connections on a printed circuit board)
  Irons vs Guns
    Irons
      Slow to heat up / slow to cool
      Precision temperature control and application with different tips
      Recommended for fine work (PCBs, solar Cells, ect.)
    Gun
      Fast to heat up / Fast to cool down
      One or two temperature settings
      Good for working on general solar car wiring
Most reliable wiring
  Crimp connectors that have been crimped and soldered with a heat shrink sleeve
    Tin wires before putting them in the heat shrink

## Slide 50: Any Questions?