## Slide 1: Building the Vehicle Frame
William Shih, Deputy Race Director

## Slide 2: Building the Vehicle Frame
Materials
Roll bar and Crush Zones
Suspension and Steering
Wheels and Brakes

## Slide 3: Material for the frame
Mild/Carbon Steel
  Really easy to work with (MIG welding)
  Inexpensive (<$1/foot)
  Heavy
  Can be easily changed/modified
  Readily accessible
  Comes in a large variety of sizes and wall thicknesses

## Slide 4: Material for the frame
Chromoly Steel
  More expensive ($4/foot) (+welding wire @ $15/lb)
  Light weight
  Can be easily changed/modified
  Comes in a large variety of sizes and wall thicknesses

## Slide 5: Material for the frame
Aluminum
  Very stiff for its weight
  Harder to weld (TIG)
  Generally tubular; notch to get better fit
  Needs more material to resist fatigue
  Can be difficult to repair

## Slide 6: Material for the frame
Titanium
  Light
  Strong (but not stiff)
  Absorbs shock
  Hard to weld
  Expensive
  Limited sizes

## Slide 7: Material for the frame
Carbon Fiber (composites)
  Lightest and stiffest
  Can be formed to any shape
  Expensive
  Needs careful planning
  Learning curve is steep
  Very hard to repair on the side of the road
  Need professional engineer certification if used for roll cage, roll bar, or crush zone

## Slide 8: Building the Vehicle Frame
Materials
Roll bar and Crush Zones
Suspension and Steering
Wheels and Brakes

## Slide 9: Roll Cage, Crush Zone, Roll Bar
Roll Cage – rigid protection encompassing entire driver; minimum OD of 1.9cm; minimum 5cm clearance to driver
Crush Zone – structural components designed to collapse on impact; minimum 15cm clearance to driver; minimum coverage
Roll Bar – protects driver in event of rollover; continuous piece of metal; minimum 5cm vertical clearance; minimum OD of 5cm; minimum wall thickness based on material; welded to frame

## Slide 10: Roll Bar Example
Front View
Side View
Continuous piece of metal
Sufficient vertical clearance

## Slide 11: Crush Zone
Crush zone must:
  be designed to absorb impact from a collision
  protect the driver from front, side, and rear collisions
  have a minimum of 15 cm of horizontal distance from all parts of the driver’s body
Teams must be able to demonstrate a specific, adequate crush zone in order to compete. Insufficient regard for structural safety will result in disqualification.

## Slide 12: Crush Zone Structure

## Slide 13: Roll Cage / Roll Bar / Crush Zone Example
Crush Zone structure – thin material designed to collapse on impact
Roll Cage – rigid protection encompassing entire driver
Roll Bar – continuous piece of metal; protects driver in event of rollover

## Slide 14: Roll Cage / Crush Zone Example
Roll Cage – good use of strong structural components; may need additional coverage for driver torso
Crush Zone – would prefer structure less rigid and deflect away from driver

## Slide 15: Building the Vehicle Frame
Materials
Roll bar and Crush Zones
Suspension and Steering
Wheels and Brakes

## Slide 16: Suspension Components
Spindle
Hub
Axle
Tie Rod

## Slide 17: Common Front Suspension Types
Solid Axle
MacPherson Strut
Dual A Arm
Notes: MacPherson
-production vehicles
-tend to be heavy
-limited adjustability
Solid Axles
-simple
-geometry is set at construction
-can be heavy
Double Arm
-most popular
-very versatile
-can be complicated with lots of options and area for mistakes

## Slide 18: Suspension/Steering Considerations
Contact Patch
  Oval shaped area where tire contacts the road
Steering Axis
  Line between two pivot points of the wheel
Ideal
Top
Side
Real
Top
Side

## Slide 19: Ackerman Steering

## Slide 20: Steering Geometry
Toe
  Angle of the wheel and tire pointing away from the centerline of the vehicle
Caster
  The angular displacement of the steering angle for the vertical axis
Camber
  The angle of the wheel and tire with respect to the vertical axis
Scrub Radius
  The distance between where the steering angle intersects the ground and the contact patch of the tire

## Slide 21: Toe Geometry
Center Line
Front
Center Line
Center Line
Neutral
In
Improves straight line stability
Out
Improves Steering Response
Can make steering “jerky”
Notes: Toe
Affects Tire Wear: want to run straight down the road – if in/out, will drag
Solar cars – affected by use of thin tires (Bridgestone Ecopia)

## Slide 22: Measuring Toe
A1
A2
B1
B2
Front
C
Dist A
Dist B
Notes: How to do proper alignment
Measure at the same spot each time

## Slide 23: Steering Geometry
Toe
  Angle of the wheel and tire pointing away from the centerline of the vehicle
Caster
  The angular displacement of the steering angle for the vertical axis
Camber
  The angle of the wheel and tire with respect to the vertical axis
Scrub Radius
  The distance between where the steering angle intersects the ground and the contact patch of the tire

## Slide 24: Caster
Front
Vertical
θ
Creates straight line stability
Positive Caster
  Steering wheel feedback
  Makes car harder to turn
  Causes wheels to self center
Negative Caster
  Unstable
Positive
Notes: No correct answer; need to set it up for the driver

## Slide 25: Steering Geometry
Toe
  Angle of the wheel and tire pointing away from the centerline of the vehicle
Caster
  The angular displacement of the steering angle for the vertical axis
Camber
  The angle of the wheel and tire with respect to the vertical axis
Scrub Radius
  The distance between where the steering angle intersects the ground and the contact patch of the tire

## Slide 26: Camber
Vertical
Negative
Vertical
Front
Positive
Affects grip and stability in cornering
Not applicable to solar car racing
Notes: Not applicable because we don’t have high speed cornering

## Slide 27: Steering Geometry
Toe
  Angle of the wheel and tire pointing away from the centerline of the vehicle
Caster
  The angular displacement of the steering angle for the vertical axis
Camber
  The angle of the wheel and tire with respect to the vertical axis
Scrub Radius
  The distance between where the steering angle intersects the ground and the contact patch of the tire

## Slide 28: Scrub Radius
Scrub Radius
Positive
Coffee Cup Experiment
Harder to Turn
Increase wear on tire
Positive
    Cause center seeking
Notes: How much force/wear for turning
Coffee cup experiment – turn cup by turning on a point vs. turning using the handle
Minimize the scrub radius to lessen energy

## Slide 29: Getting your car rolling
Building the Vehicle Frame
  Materials
  Roll bar and Crush Zones
  Suspension and Steering
  Wheels and Brakes

## Slide 30: Wheels
One of the most difficult parts to source
Choices need to be made very early in the design process
Three wheel designs:
  Lighter
  Easier to align
  Less expensive
  Not as safe

## Slide 31: Wheels
Four wheel designs
  More parts means higher cost
  Harder to get alignment correct
  Weight distribution less critical
  Much safer in the event of a flat
  Can “straddle” dead animals on the road
Required for Cruiser Division

## Slide 32: Wheels
Wheel choices (must be able to handle the weight of the car and lateral forces from turning)
  NGM wheels and tires
  Motorcycle
  Junior Dragster
  Bicycle

## Slide 33: Wheels

## Slide 34: Brakes
Solar car must have two, independent, braking systems that allow the driver to stop the vehicle safely and quickly.
  Most cars use hydraulic disk brakes
  MCP single caliper brakes are easy to install and relatively inexpensive.

## Slide 35: Brake Pedals
Brake pedals must also be independent
  Pedals, master cylinder, etc. separate for each system
Can no longer “link” pedals together
  New rules change for 2021-2022
Must be operated by foot (no hand brakes)
X

## Slide 36: Brake Testing
Brakes are tested both statically and dynamically at the event.
  Static = Test strength of brakes at rest
  Dynamic = Test how fast brakes can stop car
Many vehicles have brake problems. Brakes must be tested before you arrive at the event!

## Slide 37: Building the Vehicle Frame
William Shih, Deputy Race Director